## Slide 1: Equal Headway Instability
Project Final Presentation
Modelling and Simulating Social Systems with MATLAB
Maicol Fabbri – Cheuk Wing Edmond Lam

## Slide 2: Agenda
Introduction
Model description
Simulation results
Conclusion

## Slide 3: Scope of the Project
Urban tram system
No other traffic

## Slide 4: What does equal headway mean?
Regular intervals
Same distance
Follow schedule

## Slide 5: Why do sometimes trams arrive late?
Equal headway is unstable
Larger number of people who wants to get off the tram or board for a certain tram
Platooning effect:
Trams don’t cover uniformly the track anymore
Clusters of trams formed

## Slide 6: Research question
Can certain passenger behaviour improve the public transportation efficiency?
Ground idea: a full and delayed tram is often closely followed by an almost empty and on time tram (platooning effect)
 Instruct people to skip that tram and take the following one under specified conditions
Station
Full and delayed tram
Empty and on-time tram

## Slide 7: The model
1. Create a cyclic track
2. Add stations
5. Make people randomly arrive at the stations
3. Add trams
S
S
S
S
S
T
T
T
T
T
6. Implement tram dynamics
4. Discretize the simulation into time instants
 Vary the number of people arriving at the stations
In each instant of time:
Trams can move a cell
A well-defined number of people can board or get off the tram
A random number of people arrives at a random station each instant.
Usage of POISSON distribution with a desired mean value for the “people rate”
Number of people who wants to get off the tram is random
Boarding conditions
Trams has to wait a minimum time at each station (so to define a schedule)
When the schedule is not respected  delay
The “people rate” is used to trigger the instability.
Remark: with people rate we refer to the mean of the Poisson distribution

## Slide 8: Boarding Conditions
Case without people behaviour (control case), passengers can board if
  People on the tram who want to get off have got off
  The tram is not full
Case With people behaviour, passengers can board if
  People on the tram who want to get off have got off
  The tram is not full
  The instruction to skip the tram is not issued

## Slide 9: When to skip a tram?
We instruct people to skip a tram if:
  The incoming tram is delayed; and
  The previous tram at this station was not skipped; and
  The following tram will arrive in half of a tram period
    next tram is coming soon
    Example: if a tram takes 10 time instants to travel between two stations  half of tram period is 5
Station
Station
10 times instants length
5 time instants

## Slide 10: Simulations and result parameters
In the last instant of time, the values collected are:
  Average delay of all trams
  Average number of people waiting in all the stations
Note: 50 simulations are performed with the same boundary conditions and the results averaged
 elimination of aleatoric effects
Parameters chosen for the simulation:
Track length=50 cells
Trams=5
Stations=5, equally spaced
Tram capacity=60 people
Boarding rate=20 people/instant
Station waiting time= 3 instants
Time instants=360
People rate= 1:1:40

## Slide 11: Results – influence of people behaviour
3 Zones
Inactive zone
Active zone
Saturation zone

## Slide 12: Results – Tram delay
People behaviour drastically reduces tram delay

## Slide 13: Results – People waiting at the stations
In the “saturation zone”, the people waiting at the stations are more  the skip of a tram leads to less people carried around
Zoom in the “active zone”

## Slide 14: Results – People waiting at the stations – Active zone
People behaviour makes the trams better cover the track  in the active zone, transportation efficiency is improved
Turning points

## Slide 15: Results – Trams delay – Active zone
Reduction of ~90%
Reduction of ~90%
X: 24
Y: ~70
X: 25
Y: ~85
X: 24
Y: ~6.5
X: 24
Y: ~8.5

## Slide 16: Conclusion
People behaviour can have a huge positive influence in the public transportation efficiency
Choosing to wait few minutes more can brings benefits to all the other passengers
Dilemma: maximizing own profit or cooperate for a collective gain?
Remark: the numerical values shown strongly depends on the boundary conditions imposed. Nevertheless, several tries with different boundary conditions and parameters have shown the same positive results

## Slide 17: Thank you for your attention